Users’ guide to
High-resolution Cloud Analysis Information

November 2015

Japan Meteorological Agency

Users’ guide to High-resolution Cloud Analysis Information

- Introduction

This users’ guide is for High-resolution Cloud Analysis Information (HCAI) – a satellite-derived cloud analysis product based on Himawari observation results. HCAI provides grid point data with cloud classification indices and cloud altitude values. Chapter 2 outlines the data format, Chapter 3 gives details of the product, and Chapter 4 highlights points to note. This guide relates to HCAI only.

- Data format

HCAI is provided in FM92 GRIB edition 2 format (i.e., processed data expressed as binary grid-point values) as described in the WMO Manual on Codes. Files contain data on just one meteorological parameter (i.e., they are single GRIB2 files). Appendix A outlines the data format.

- Contents

(1) Region

The region of HCAI coverage is shown in Appendix B.

(2) Meteorological parameters

The meteorological parameters in the product are cloud mask, snow ice mask, cloud type, cloud top height (all derived from objective analysis of Himawari observation data) and quality control information.

a) Cloud mask (including dust mask)

This parameter relates to the presence of cloud and dust. Table 1 lists cloud mask code numbers.

Table 1  Cloud mask code numbers

| Cloud mask | Code number |
| --- | --- |
| Clear (no cloud), no dust | 200 |
| Clear/cloud, no dust | 201 |
| Cloud, no dust | 202 |
| Clear, dust | 205 |
| Clear/cloud, dust | 206 |
| Cloud, dust | 207 |

b) Snow ice mask

This parameter relates to the presence of snow ice. It is given as “11” to indicate the presence of snow ice and as “0” to indicate absence.

c) Cloud type

This parameter relates to one of eight cloud types (clear (no cloud), cumulonimbus, dense cloud, upper cloud, middle cloud, cumulus, stratocumulus and stratus/fog). Table 2 lists cloud type code numbers.

Table 2  Cloud type code numbers

| Cloud type | Code number |
| --- | --- |
| Clear (no cloud) | 0 |
| Cumulonimbus | 1 |
| Dense cloud | 200 |
| Upper cloud | 201 |
| Middle cloud | 202 |
| Cumulus | 4 |
| Stratocumulus | 3 |
| Stratus or fog | 204 |

Upper cloud 	Single-layer cloud with a top height above 400 hPa

Middle cloud 	Cloud with a top height between 400 and 600 hPa

Cumulus 	Convective cloud with a top height below 600 hPa

Dense cloud 	Cloud with a top height above 400 hPa (other than cumulonimbus and upper cloud)

d) Cloud top height

This parameter relates to cloud-top height in hundreds of meters.

e) Quality control information

This parameter relates to HCAI quality control. Table 3 lists the details of the information. It is given as “0” to indicate the possibility of high quality and as “1” to indicate the possibility of low quality for each bit in order from the least significant bit.

Table 3  Quality control information summary

| Bit no. | Quality control information | 0 | 1 |
| --- | --- | --- | --- |
| 1 | Validity of quality flag | Valid | Invalid |
| 2 | Quality loss due to effects of the sun | No possibility | Some possibility |
| 3 | Quality loss due to effects of the moon | No possibility | Some possibility |
| 4 | Solar calibration operation | Not in operation | In operation |
| 5 | Solar eclipse operation | Not in operation | In operation |
| 6 | Quality of cloud mask | High quality | Low quality |
| 7 | Quality of cloud type | High quality | Low quality |
| 8 | Quality of cloud top height | High quality | Low quality |

- Points to note

- There may be discrepancies between HCAI and surface synoptic observation data due to differences in observation methods.

- Clouds too small for the spatial resolution of satellite observation (2 km at the sub-satellite point), known as sub-pixel clouds, cannot be detected.

- Lower convective clouds with the same brightness temperature as the background cannot be detected.

- Very thin upper clouds, known as semi-transparent clouds, may remain undetected.

- Cumulus, stratocumulus and stratus/fog may be incorrectly classified.

- Cloud classification in the border area between daytime and nighttime is currently being improved.

- The specifications of HCAI may be changed with notice.

Appendix A

GRIB2 format and templates

| Section number | Section name or template applied | Octet | Content | Table | Value | Remark |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | Indicator Section | 1 – 4 | GRIB |  | GRIB | International Alphabet No. 5 (CCITT IA5) |
|  |  | 5 – 6 | Reserve |  | 0xFFFF | Missing |
|  |  | 7 | Discipline-GRIB master table number | Code table 0.0 | 0 | Meteorological product |
|  |  | 8 | GRIB edition number |  | 2 |  |
|  |  | 9 – 16 | Total length of GRIB message in octets |  | 11381930 |  |
| 1 | Identification Section | 1 – 4 | Length of section in octets |  | 21 |  |
|  |  | 5 | Section number |  | 1 |  |
|  |  | 6 – 7 | Identification of originating/generating center |  | 34 | Tokyo |
|  |  | 8 – 9 | Identification of originating/generating sub-center |  | 0 |  |
|  |  | 10 | GRIB master table version number | Code table 1.0 | 2 | Currently operating version number |
|  |  | 11 | GRIB local table version number | Code table 1.1 | 1 | Local Table Version 1 |
|  |  | 12 | Reference time significance | Code table 1.2 | 3 | Observation time |
|  |  | 13 – 14 | Data reference time (year) |  | (Variable) | See #1 |
|  |  | 15 | Data reference time (month) |  | (Variable) | See #1 |
|  |  | 16 | Data reference time (day) |  | (Variable) | See #1 |
|  |  | 17 | Data reference time (hour) |  | (Variable) | See #1 |
|  |  | 18 | Data reference time (minute) |  | (Variable) | See #1 |
|  |  | 18 | Data reference time (second) |  | (Variable) | See #1 |
|  |  | 20 | Product status of processed data in current GRIB message | Code table 1.3 | 0 | Operational products |
|  |  | 21 | Type of processed data in current GRIB message | Code table 1.4 | 6 | Processed satellite observation |
| 2 | Local Use Section | Not used |  |  | Omission |  |
| 3 | Grid Definition Section | 1 – 4 | Section length in octets |  | 72 |  |
|  |  | 5 | Section number |  | 3 |  |
|  |  | 6 | Grid definition source | Code table 3.0 | 0 | See code table 3.1 |
|  |  | 7 – 10 | Number of data points |  | 11381751 |  |
|  |  | 11 | Number of octets for optional list of numbers defining number of points |  | 0 |  |
|  |  | 12 | Interpretation of list of numbers defining number of points |  | 0 |  |
|  |  | 13 – 14 | Grid definition template number | Code table 3.1 | 0 | Latitude/longitude |
|  | Template 3.0 | 15 | Shape of earth | Code table 3.2 | 4 | Oblate spheroid as defined in IAG-GRS80 model |
|  | ↓ | 16 | Scaled factor of spherical-earth radius |  | 0XFF | Missing |
|  | ↓ | 17 – 20 | Scaled value of spherical-earth radius |  | 0xFFFFFFFF | Missing |
|  | ↓ | 21 | Scaled factor of oblate spheroid earth’s major axis |  | 1 |  |
|  | ↓ | 22 – 25 | Scaled value of oblate spheroid earth’s major axis |  | 63781370 |  |
|  | ↓ | 26 | Scaled factor of oblate spheroid earth’s minor axis |  | 1 |  |
|  | ↓ | 27 – 30 | Scaled value of oblate spheroid earth’s minor axis |  | 63567523 |  |
|  | ↓ | 31 – 34 | Ni-number of points along a parallel |  | 3251 |  |
|  | ↓ | 35 – 38 | Nj-number of points along a meridian |  | 3501 |  |
|  | ↓ | 39 – 42 | Basic angle of initial production domain |  | 0 |  |
|  | ↓ | 43 – 46 | Subdivision of basic angle used to define extreme longitudes and latitudes, and direction increments |  | 0xFFFFFFFF | Missing |
|  | ↓ | 47 – 50 | La1-latitude of first grid point | 10**-6 degree unit | 55000000 | 55.0 degrees north |
|  | ↓ | 51 – 54 | Lo1-longitude of first grid point | 10**-6 degree unit | 90000000 | 90.0 degrees east |
|  | ↓ | 55 | Resolution and component flags | Flag table 3.3 | 0x30 |  |
|  | ↓ | 56 – 59 | La2-latitude of last grid point | 10**-6 degree unit | 15000000 | 15.0 degrees south |
|  | ↓ | 60 – 63 | Lo2-longitude of last grid point | 10**-6 degree unit | 155000000 | 155.0 degrees east |
|  | ↓ | 64 – 67 | Di-i direction increment | 10**-6 degree unit | 20000 | 0.02 degrees |
|  | ↓ | 68 – 71 | Dj-j direction increment | 10**-6 degree unit | 20000 | 0.02 degrees |
|  | Template 3.0 | 72 | Scanning mode | Flag table 3.4 | 0x00 |  |
| 4 | Product Definition Section | 1 – 4 | Section length in octets |  | 34 |  |
|  |  | 5 | Section number |  | 4 |  |
|  |  | 6 – 7 | Number of coordinate values after template |  | 0 |  |
|  |  | 8-9 | Product definition template number | Code table 4.0 | 0 | Analysis or forecast at a horizontal level or in a horizontal layer at a point in time |
|  | Template 4.0 | 10 | Parameter category | Code table 4.1 | 6 | Cloud |
|  | ↓ | 11 | Parameter number | Code table 4.2 | (Variable) | See #2 |
|  | ↓ | 12 | Generation process type | Code table 4.3 | 0 | Analysis |
|  | ↓ | 13 | Background generation process identifier |  | 0xFF | Missing |
|  | ↓ | 14 | Analysis of forecast generation process identifier |  | 0xFF | Missing |
|  | ↓ | 15 – 16 | Hour of observational data cut-off point after reference time |  | 0 |  |
|  | ↓ | 17 | Minute of observational data cut-off point after reference time |  | 10 |  |
|  | ↓ | 18 | Time range unit indicator | Code table 4.4 | 0 | Minutes |
|  | ↓ | 19 – 22 | Forecast time in units as defined by octet 18 |  | 0 |  |
|  | ↓ | 23 | Type of first fixed surface | Code table 4.5 | 3 | Cloud-top level |
|  | ↓ | 24 | Scaled factor of first fixed surface |  | 0xFF | Missing |
|  | ↓ | 25 – 28 | Scaled value of first fixed surface |  | 0xFFFFFFFF | Missing |
|  | ↓ | 29 | Type of second fixed surface | Code table 4.5 | 0xFF | Missing |
|  | ↓ | 30 | Scaled factor of second fixed surface |  | 0xFF | Missing |
|  | Template 4.0 | 31 – 34 | Scaled value of second fixed surface |  | 0xFFFFFFFF | Missing |
| 5 | Data Representation Section | 1 – 4 | Section length in octets |  | 21 |  |
|  |  | 5 | Section number |  | 5 |  |
|  |  | 6 – 9 | Total number of data points |  | 11381751 |  |
|  |  | 10 – 11 | Data representation template number | Code table 5.0 | 0 | Grid point data – simple packing |
|  | Template 5.0 | 12 – 15 | Reference value (R) |  | 0.0 | IEEE 32-bit floating-point value |
|  | ↓ | 16 – 17 | Binary scale factor (E) |  | 0 |  |
|  | ↓ | 18 – 19 | Decimal scale factor (D) |  | (Variable) | See #2 |
|  | ↓ | 20 | Number of bits used for each packed value for simple packing |  | 8 |  |
|  | Template 5.0 | 21 | Type of original field value | Code table 5.1 | 1 | Integer |
| 6 | Bit-map Section | 1 – 4 | Section length in octets |  | 6 |  |
|  |  | 5 | Section number |  | 6 |  |
|  |  | 6 | Bit-map indicator |  | 0xFF | Missing |
| 7 | Data Section | 1 – 4 | Section length in octets |  | 11381756 |  |
|  |  | 5 | Section number |  | 7 |  |
|  | Template 7.0 | 6 – nn | Binary data values – binary string with each scaled data value |  | (Variable) | Data in format described by Data Template 7.0. 0xFF = Missing |
| 8 | End Section | 1 – 4 | 7777 |  | "7777" | International Alphabet No. 5 (CCITT IA5) |

| #1 Temporal representation |  |
| --- | --- |
| Reference time | Value |
| Year | (4-digit integer) |
| Month | 1 – 12 |
| Day | 1 – 31 |
| Hour | 0 – 23 |
| Minute | 0 – 59 |
| Second | 0 – 59 |
| Coordinated Universal Time (UTC) is used. |  |

| #2 Parameter numbers |  |  |  |
| --- | --- | --- | --- |
| Product element | Parameter number | Decimal scaled factor (D) | Remark |
| Cloud mask | 201 | 0 | See #3 |
| Snow ice mask | 202 | 0 | See #4 |
| Cloud type | 8 | 0 | See #5 |
| Cloud top height (m) | 12 | -2 |  |
| Quality control information | 200 | 0 | See #6 |

| #3 Cloud mask code numbers |  |
| --- | --- |
| Cloud mask | Code number |
| Clear (no cloud), no dust | 200 |
| Clear/cloud, no dust | 201 |
| Cloud, no dust | 202 |
| Cloud, dust | 205 |
| Clear/cloud, dust | 206 |
| Cloud, dust | 207 |

| #4 Snow ice mask code numbers |  |
| --- | --- |
| Snow ice mask | Code number |
| No snow ice | 0 |
| Snow ice | 11 |

| #5 Cloud type code numbers |  |
| --- | --- |
| Cloud type | Code number |
| Clear (no cloud) | 0 |
| Cumulonimbus | 1 |
| Dense cloud | 200 |
| Upper cloud | 201 |
| Middle cloud | 202 |
| Cumulus | 4 |
| Stratocumulus | 3 |
| Stratus or fog | 204 |

| #6 Summary of quality control information bits |  |
| --- | --- |
| Quality control information | 0 | 1 |
| Validity of quality flag | Valid | Invalid |
| Quality loss due to effects of the sun | No possibility | Some possibility |
| Quality loss due to effects of the moon | No possibility | Some possibility |
| Solar calibration operation | Not in operation | In operation |
| Solar eclipse operation | Not in operation | In operation |
| Quality of cloud mask | High quality | Low quality |
| Quality of cloud type | High quality | Low quality |
| Quality of cloud top height | High quality | Low quality |

Appendix B

Region

HCAI for Malaysia covers the area from latitude 55 degrees north to 15 degrees south and from longitude 90 degrees to 155 degrees east. Each grid square covers 0.02 degrees in latitude and longitude. There are 3,501 grid squares in latitude and 3,251 in longitude. A map of the region is shown below.

# Comments

If these are regular count numbers, they should have comma separators (i.e., “11,381,751”). Same below/above.

Original meaning unclear - this change needs to be verified.

“degrees west”?

# Text boxes

3,251 grid squares

3,501 grid squares

(55°N, 90°E)

(15°S, 155°E)

Figure 1  Region of High-resolution Cloud Analysis Information for Malaysia